## Slide 1: Uterine Evacuation via Vacuum Aspiration
Postabortion Care Curriculum
Module 2, Session 5

## Slide 2
The contents of this presentation draw from the Postabortion Care Curriculum Reference Manual.
Please refer to the Reference Manual for additional information, including further details and guidance as well as compete references to source material.

## Slide 3
At the end of this session, participants will be able to:​
Identify the parts of MVA equipment and select the correct size syringe and cannula.
If locally applicable, for EVA and/or FSE:
  Identify the parts of the EVA and/or FSE equipment
  Select the correct size cannula
Demonstrate the ability to assemble, test, and prepare MVA, EVA, or FSE equipment.
Perform the VA procedure using MVA, EVA, or FSE, according to the steps outlined.
Demonstrate appropriate counseling before, during, and after the procedure.
Recognize and solve technical and/or procedural problems.
Record complete, accurate case information in client charts, logbooks, and other forms.
Learning Objectives

## Slide 4
  Manual vacuum aspiration (MVA) uses a hand-held vacuum syringe and flexible plastic cannula to perform the evacuation. This method does not require electricity.
Types of VA Methods
Source: Powell and Kapp. 2019

## Slide 5
  Foot pump suction (FSE) uses a foot pump suction evacuator with a flexible plastic cannula to obtain vacuum and perform the evacuation, using either intermittent or continuous suction. This method does not require electricity.
Types of VA Methods (continued)
Source: Ningbo Tianhou Importers and Exporters Co. Ltd

## Slide 6
  Electric vacuum aspiration (EVA) uses an electric pump and cannula to evacuate the uterus using either intermittent or continuous suctioning. This method requires reliable electricity.
Types of VA Methods (continued)
Source: Apex International. n.d.

## Slide 7
  How It Works
  The provider generates the vacuum in the syringe.
  The provider inserts a sterile cannula into the uterine cavity through the cervix.
  The provider connects the syringe to the cannula.
  The provider releases the valve, and through the established suction, empties the contents of the uterus into the syringe.
  When the syringe becomes full, the provider detaches and empties it, and generates vacuum again before reconnecting to the cannula and repeating the process.
MVA Basics

## Slide 8
  Equipment Benefits
  It does not require electricity.
  It is portable.
  The syringe holds 60 cc of aspirate fluid and tissue.
  Single-valve, double-valve, and MVA Plus® syringes are compatible with other cannulae.
  Reusable, but requires cleaning and decontamination.
MVA Basics (continued)

## Slide 9
Basic Components of an MVA Kit
Source: EngenderHealth. 2004.

## Slide 10
Basic Components of an MVA Kit (continued)
Source: EngenderHealth. 2004.
  Exercise:
  Label each part of the kit, as numbered.

## Slide 11
Basic Components of an MVA Kit (continued)
Source: EngenderHealth. 2004.
  Exercise Answers

## Slide 12
Greet the client and perform a rapid assessment, ruling out or treating complications and ensuring the client is stable.
Assess the client.
  Obtain the client’s history.
  Perform physical and pelvic examinations, assessing the uterine size.
  Request any necessary laboratory or other testing.
  Rule out any contraindications.
  Review precautions, as appropriate.
  Explain findings and emergency treatment options and allow the client to make an informed decision.
Pre-Procedure Care

## Slide 13
Provide counseling, emotional support, and encouragement.
  Discuss pain management options with the client.
  Provide contraceptive counseling.
  Provide additional counseling as appropriate.
Obtain consent for the procedure, pain management plan, and contraception.
Organize the procedure area and team.
  Ensure all necessary equipment are available and sterilized.
  Ensure required medications and contraceptive kits are available.
  Ensure each surgical team member is in place.
  Perform hand hygiene and don personal protective attire.
Pre-Procedure Care (continued)

## Slide 14
Prepare the client for the procedure.
  Ask the client to empty their bladder and clean their perineum, if able.
  Help the client onto the table, lying in a lithotomy position; drape the client.
  Administer medication, as indicated in the pain management plan.
Implement infection prevention measures.
Pre-Procedure Care (continued)

## Slide 15
MVA Instruments
Select and inspect cannulae.
  Identify several cannulae of different sizes.
  Select cannulae according to the uterine size; the cannula needs to be large enough to allow passage of tissue expected and to fit snugly through the cervix.
  Inspect selected cannulae for cracks or other defects; discard if there are any signs of weakness or wear and identify another cannula for inspection and use.
  Select the appropriate adapter, if needed.
Instrument Preparations

## Slide 16
Select and inspect syringes and adapters, if required.
  Prepare 2 syringes, recognizing that the amount of blood and tissue in the uterus can be unpredictable.
  Ensure that the colored dots on the cannula match the color of the adapter, if applicable.
  Ensure the syringe can hold a vacuum. Apply lubricant to or replace the O-ring of syringes unable to hold a vacuum. Discard any syringes with cracks or defects or that do not hold a vacuum and identify alternate syringes for inspection and use.
  Attach the adapter, if required, to the end of the syringe or cannula.
Instrument Preparations (continued)

## Slide 17
Instrument Preparations (continued)
Cannula, Adapter, and Syringe Attributes |  | 
Cannula Size | Adapter Color | Syringe Type
4, 5, 6 mm | No adapter required | Single*
4, 5, 6 mm | Blue | Double
7 mm | Tan | Double
8 mm | Ivory | Double
9 mm | Dark Brown | Double
10 mm | Dark Green | Double
12 mm | No adapter required | Double
*No longer available in most settings |  | 
Approximating Uterine Size and Selecting Cannula Size | 
Approx. Uterine Size | Approx. Cannula Size
5 to 7 weeks | 5 mm
7 to 9 weeks | 6 mm
9 to 12 weeks | 7 to 12 mm
*Weeks since last menstrual period | 

## Slide 18
Check the plunger and valve on the syringe. The plunger should be positioned all the way into the barrel, with the pinch valve open and the valve button out.
Close the pinch valve by pushing the button down and forward until it locks into place.
Prepare the syringe.
  Grasp the barrel and pull the plunger back until the arms snap outward.
  Ensure the plunger arms are fully secured, so the plunger cannot move forward involuntarily. Incorrect positioning could allow the arms to slip back inside the barrel; improperly securing only one arm of the plunger can lead to breakage.
  Never grasp the syringe by the plunger arms.
Instrument Preparations (continued)

## Slide 19
Confirm and prepare the syringe vacuum.
  Establish vacuum and leave the syringe for several minutes with the vacuum established.
  Open the pinch valve—listen for a rush of air into the syringe indicating that there was a vacuum in the syringe.
  If the syringe failed to maintain vacuum, identify a new syringe and repeat the test.
  Reestablish the vacuum in the syringe for use during the procedure.
Instrument Preparations (continued)

## Slide 20
EVA and FSE Instruments
Identify several cannulae of different sizes.
  Select cannulae according to the uterine size; the cannula needs to be large enough to allow passage of tissue expected and to fit snugly through the cervix.
  Inspect selected cannulae for cracks or other defects; discard if there are any signs of weakness or wear and identify another cannula for inspection and use.
  Check that the EVA or FSE equipment creates a vacuum.
Instrument Preparations (continued)

## Slide 21
Step 1: Prepare for the Procedure
Counsel the client about the treatment options, pain management plan, and contraceptive options. Verify that the client has provided consent as required.
Prepare the client for the procedure, including by:
  Asking the client to empty their bladder and clean their perineum, if able.
  Helping the client onto the table and into position; drape the client.
  Administering pre-procedure medication, per the pain management plan.
The Procedure: Step-by-Step

## Slide 22
Step 1 (continued)
Ensure that:
  Emergency equipment and supplies (including medication) are available.
  Emergency back-up is available.
  Instruments are sterilized and assembled on the sterile field.
  Contraceptive methods are available in the treatment room.
Perform hand hygiene and don personal protective attire.
Perform a bimanual exam to determine uterine size, position, and degree of cervical dilation. Confirm size less than 14 weeks.
The Procedure: Step-by-Step (continued)

## Slide 23
Step 1 (continued)
Insert a vaginal speculum and visualize the cervix.
Apply an antiseptic solution to the cervix and vagina using the no-touch technique.
Check the cervix for tears or protruding products of conception. If any are present in the vagina or cervix, remove using ring or sponge holding forceps.
Gently apply a vulsellum or single toothed tenaculum to the anterior lip of the cervix.
The Procedure: Step-by-Step (continued)

## Slide 24
Step 2: Dilatate the Cervix, if Indicated
Assess the need for pain management and provide appropriate care—including, as necessary, paracervical block—before proceeding.
Begin dilatation by using the smallest dilator and progress to the largest dilator that ensures adequate dilatation.
Be extremely careful not to tear the cervix or create a false opening.
Step 3: Insert the Cannula
Step 4: Measure the Uterus
The Procedure: Step-by-Step (continued)

## Slide 25
Step 5: Evacuate the Uterus via MVA
Prepare the syringe (establish vacuum).
Attach the syringe to the cannula, being careful not to push it further into the uterus.
Release the pinch valve(s) to transfer the vacuum and evacuate the uterine contents.
Check for signs of completion.
Detach the syringe, remove the tenaculum and speculum, withdraw the cannula. Place instruments into a container with clean water.
Perform a bimanual exam to check uterus firmness and size. Repair any cervical tears.
Inform the client that you have completed the procedure.
If the client requested an implant or intrauterine device (IUD), complete the insertion.
The Procedure: Step-by-Step (continued)

## Slide 26
Step 5: Evacuate the Uterus via EVA and FSE
Attach the cannula to the suction source.
Evacuate the uterine contents.
To avoid losing vacuum, do not to withdraw cannula opening beyond the cervical os. If the vacuum is lost, reestablish the vacuum before continuing.
Check for signs of completion.
Detach the vacuum source. Remove and place instruments in clean water.
Perform a bimanual exam to check uterus firmness and size. Repair any cervical tears.
Inform the client that you have completed the procedure.
If the client requested an implant or IUD, complete the insertion.
The Procedure: Step-by-Step (continued)

## Slide 27
Step 6: Inspect the Tissue
Inspect the tissue removed from the uterus to determine the volume of blood, clots, and products of conception.
Examine the products of conception to ensure complete evacuation and to check for a molar pregnancy. If no products of conception are visible:
  The client may have already voided the products of conception.
  The uterine cavity may still contain products of conception. Repeat the procedure.
  The client’s vaginal bleeding may be the sign of another health problem.
  The client may have an ectopic pregnancy.
  The uterus may be abnormal, such as in a double uterus (rare).
The Procedure: Step-by-Step (continued)

## Slide 28
Clients with uncomplicated cases may be discharged within 1 or 2 hours. The client may be discharged when they are stable, can walk without assistance, and have received post-procedure counseling and services.
Complete the following tasks before discharge:
Check vital signs before removing the client from the procedure area.
Discuss the client’s pain level and administer medication(s) as needed.
Administer oxytocin, ergometrine, or misoprostol.
Check for vaginal bleeding at least once before discharge.
Confirm that any cramping has declined; prolonged cramping is not normal.
Encourage client to eat, drink, and walk around, as they are comfortable doing so.
Post–Procedure Care

## Slide 29
Explore the client’s feelings and concerns and provide additional care and support.
Instruct the client not to have intercourse or to put anything into their vagina until after the bleeding stops.
Instruct the client on when they may resume chores and work.
Instruct the client to watch for signs and symptoms requiring immediate attention.
Complete or update client charts and other forms, as required.
Post–Procedure Care (continued)
  Reminder: PAC is incomplete without voluntary contraceptive counseling and service provision.

## Slide 30
Before the Procedure
Perform hand hygiene.
Don personal protective equipment.
Drape the client.
Cleanse the cervix and vagina with an antiseptic solution.
During the Procedure
Use sterile instruments and equipment.
Use gentle surgical techniques.
Infection Prevention

## Slide 31
After the Procedure
Undertake proper waste management tasks.
Remove surgical gloves and wash hands thoroughly with soap and water.
Provide post-procedure instructions to the client.
Administer antibiotics, as applicable.
Infection Prevention (continued)

## Slide 32
Providers may face various problems when performing and after completing VA procedures.
This includes technical problems with equipment and medical problems with the procedure.
Most problems are not serious, and, if recognized and corrected or treated immediately, will not affect client results or recovery.
Managing Common Problems
  Reminder: Problems can occur even under ideal circumstances. Identifying issues early and acting immediately are key to success.

## Slide 33
Full Syringe
Close the pinch valve of the syringe.
Disconnect the syringe, leaving the tip of the cannula inside the uterus.
Empty the syringe into a container for later inspection.
If you only have one syringe available, reestablish the vacuum in the syringe, reconnect it to the cannula, and resume the aspiration.
Alternately, if there is a second prepared syringe available, switch syringes.
Technical Problems with Equipment

## Slide 34
Cannula Withdrawn Prematurely
For MVA:
Remove the syringe and cannula.
Close the pinch valve of the syringe.
Disconnect and empty the syringe.
Reestablish the vacuum or use another prepared syringe.
Reinsert the cannula if not contaminated or insert a new sterile cannula.
Reconnect the syringe to the cannula, release the valve, and continue.
Technical Problems with Equipment (continued)
For FSE or EVA:
Switch off the vacuum pump or machine and disconnect the tubing.
Reinsert the cannula if not contaminated or insert a new sterile cannula.
Reconnect the tubing to the vacuum and switch on or release the vacuum.

## Slide 35
Cannula Clogged
For MVA:
Close the pinch valve of the syringe.
Remove the syringe and cannula.
Remove material from the cannula.
Reinsert the cannula or insert a new sterile cannula.
Reestablish the vacuum or use another prepared syringe.
Reconnect the syringe to the cannula, release the valve, and continue.
Technical Problems with Equipment (continued)
For FSE or EVA:
Switch off the vacuum.
Remove the cannula.
Remove material from the cannula.
Reinsert the cannula or insert a new sterile cannula.
Switch on the vacuum and continue.

## Slide 36
Syringe Does Not Maintain Vacuum
Lubricate the plunger and barrel with a drop of silicone.
If this does not work, replace the O-ring.
If this does not work, use another syringe.
Plunger Arm Breaks
Replace the syringe and plunger immediately and continue.
Avoid this by being gentle when creating the vacuum and ensuring both plunger arms are out of the barrel before releasing the plunger.
Technical Problems with Equipment (continued)

## Slide 37
Less Tissue than Expected
This may indicate either:
Client already voided the products of conception before the procedure.
Client’s vaginal bleeding is not due to pregnancy nor to an incomplete abortion.
Client has an ectopic pregnancy.
Incomplete Evacuation
Avoid this by using the correct size cannula and watching for signs of completion.
If this occurs, repeat the evacuation.
Medical Problems with the Procedure

## Slide 38
Uterine Perforation (rare)
Signs include cannula going through the uterine cavity beyond the expected uterine size, continuous and persistent vaginal bleeding, abdominal distension and/or rigidity, cervical motion tenderness, and shoulder pain.
Vaginal Bleeding Not Due to Pregnancy
This may occur because of:
Estrogen-breakthrough bleeding
Progesterone-breakthrough bleeding
Uterine fibroids
Medical Problems with the Procedure (continued)

## Slide 39
Ectopic Pregnancy
Ectopic pregnancies can become dangerous (even deadly) if not treated quickly.
Signs include adnexal mass, fullness or bogginess in the pouch of Douglas, and/or hemoperitoneum. Quickly prepare client for referral if surgery is unavailable on-site.
A client with a history of any of the following is at higher risk:
  Previous ectopic pregnancy or pregnancies
  Pelvic infections
  IUD or progestin-only contraceptive use
Medical Problems with the Procedure (continued)